## Slide 1
Flow Chemistry
- an overview
Peter J. Joyce
Systems Integration Director
Sentinel Process Systems
Hatboro, PA
pjj@kilolabs.com
215-528-2079
Presentation to the
Chemical Consultants Network
Jan 9, 2019

## Slide 3
Batch vs Continuous Operation – Simple Comparison
10cc Reactor Volume - Surface Area / Volume Ratio
Volumetric Flask 1.8
Coiled Reactor 25.1
Heat Removal in an Exothermic reaction
Q = U x A x ΔT
Q - Heat Release – Kcal/hr
U – Heat transfer coefficient – Kcal/(M2-Hr-deg C)
A – Heat transfer area – M2
ΔT - Differential Temp between reactants and heat transfer fluid, deg C
Result - needed ΔT plummets!

## Slide 4: What is flow (tube) chemistry?
Performing a reaction continuously, small > large scale
through either a coil, static mixer or fixed bed reactor.
OR
Pump reactants
Reactor
Product collection

## Slide 6
Reactor Types and Strategies
Flow Tube
Homogeneous, non-precipitating, reaction screening, low pressure drop
Micro Channel Reactor – Integral Static Mixers
Direct Scale up path to tons/day, High Mixing, non-precipitating, excellent heat transfer
(External) Agitated Reactors
Good for slurries/ solids, plug flow at low throughput, no seals or drive shaft
Spinning Disk Reactors
Extremely high shear mixing, highly exothermic reactions, at short residence times.

## Slide 7
Prior to production, the reaction was optimised in Labtrix® (10 ml);
Base stoichiometry (0.2 eq.)
Reaction time (1.5 min)
Equal solution flow rates
Reactor temperature 90 ºC
Under these pre-defined conditions, KiloFlow® was used to produce the condensation product;
Operating for 3 h, 89.31 g of (Z)-ethyl-2-cyano-3-phenylacrylate was obtained in high yield;
  Upon precipitation with DI H2O (98.7 % yield)
Production using KiloFlow®:
Synthesis of (Z)-Ethyl-2-cyano-3-phenylacrylate
x 7300
Notes: 7

## Slide 8
Labtrix™
µg to mg
300µm channel width
KiloFlow™
g to kg
1mm channel width
Plantrix EKasic® Industrial Reactor
kg to tonnes,
(2-5 mm channel width)
Scalability is Key at all Stages

## Slide 9
Flow guided between modules by Teflon interconnections
2 temperature zones
Mixer (red) & residence or Quench modules (blue) can be at different temperatures
Plantrix®:
Flexible Reactor Set-up
1X (Residence I)
3X (Residence II)
1X (Mixer)
Example system setup
1X (Quench)
Notes: 9

## Slide 10
Efficient mixing essential in flow chemistry
Static glass mixers – can also be used as reactors
Made from borosilicate glass with pre-tempering channels and extended mixing domain.
Temperature range -80⁰ to 260⁰C
Can withstand up to 40bar
‘Easy’ standard HPLC screw connectors with Perlast ‘O’-ring sealing system
Different sizes (1.6, 1.0 and 0.27 mL)
2 input [A+B] and 3 input [(A+B)+C] options
Residence time chips available 15 ml and 20 ml
Glass Static Mixer/Reactor Chips
© Uniqsis Ltd 2017.

## Slide 11
Coil and fixed bed column reactor options
Selection of Omnifit glass column reactors
Sizes: 10mm, 15mm, 20mm OD x100mm
Adjustable plunger, PTFE/PEEK construction (Tmax=150oC Pmax 60 bar)
Stainless steel available on request
Wide selection of coil reactors
Sizes: 2.0ml to 60 ml
Materials: PTFE, PFA, 316L SS, Hastelloy C, Copper
1/16” or 1/8” tubing options available, thin and thick wall options
© Uniqsis Ltd 2017.

## Slide 12
Uniqsis FlowSyn™ Multi-X flow reactor systems
Programs up to 10 separate experiments
Vary flow rates, temperatures, residence times
No additional computer required
‘fractionate’ & ‘optimise’ sample collection modes
© Uniqsis Ltd 2017
.

## Slide 13
A + B
pre-
collect
post-
collect
A + B + pre + post
Time
Concn
Collect All: Positive Pre- and Post-collect
© Uniqsis Ltd 2017.

## Slide 14
A + B
pre-
collect
post-
collect
A + B - pre - post
Time
Concn
Collect Only Steady State: Negative Pre- and Post-collect
© Uniqsis Ltd 2017.

## Slide 15
PhotoSyn Photochemical reactor
Blue light LED’s hemispherical arrays peaking 455 nm (range 330 to 550 nm) 720 W
Integral cooling for optics requires water line and input/output for chiller to cool reactor
Scale up route with larger reactor coil (high power)
Suitable for photoredox/photocatalysis applications
© Uniqsis Ltd 2017

## Slide 16
In-line UV-Vis detector – monitor steady state
Short path length, in-line high pressure flow cell uses PFA reactor tubing
Fibre optic connections permit positioning anywhere in the flow path
Range: 220-860nm, NIR option available to 1100nm (0.1 to 3A)
Enhanced 3648 CCD array detector (Full scan 2 seconds)
5 user selectable wavelengths to avoid detector saturation at typical reaction concentrations
Compact footprint, approx. 20 cm3
Essential for monitoring concentration to achieve steady state
© Uniqsis Ltd 2017.

## Slide 18: Coflore transverse mixing
Efficient radial mixing
No baffles (self baffling)
No seals or magnetic couplings
No centrifugal effects
No shaft stability problems
©AM Technology 2012
Patented technology
Agitated Cell Reactor
Agitated Tube Reactor

## Slide 19: Coflore ACR – Lab scale
Product flow
Reaction cell
Inter-stage channel
Discharge
Feed
Lab scale
Ten reaction cells cut within a monolithic block
©AM Technology 2012
Patented technology

## Slide 20: Coflore ATR – Industrial scale
Operating capacity - 1 to 10 litres
10 temperature zones
Industrial scale Coflore systems use the same mixing technique but the reaction cells are expanded into long tubes
Patents pending
©AM Technology 2012
Patented technology

## Slide 21
Energy dissipation in Spinning Disk Reactors
Meeuwse, M., van der Schaaf, J. and Schouten, J. C. (2012), Multistage rotor-stator spinning disc reactor. AIChE J., 58: 247–255. doi: 10.1002/aic.12586
Similar in Energy Dissipation to Microreactors
Heat Transfer is not tied to Mass Transfer
Mixing is not controlled by the net flow

## Slide 22
Synthetron ™ Spinning Disk Reactor

## Slide 23: Reaction Examples: Halogen/Lithium Exchange
Batch | Synthetron
97% Yield | 98% Yield
-78 C required, slow addition | Scalable, room temp 2.7 Kg/hr
Feed reagent concentrations of 2.0M, lithium products were quenched with TMSCl and analyzed by GC.
Tet. Lett., 2010, 51, p. 4793.

## Slide 24
Flow chemistry reaches manufacturing milestone
Lilly chemists make chemotherapy drug candidate in a multistep continuous flow process using current Good Manufacturing Practices
By Bethany Halford
Volume 95 Issue 25 | p. 7 | News of The Week Issue Date: June 19, 2017 | Web Date: June 16, 2017 (C&E News)
Continuous Manufacturing: A Changing Processing Paradigm
Apr 01, 2015
By Randi Hernandez
BioPharm International
GSK doubles down on Singapore continuous processing plant
June 29, 2015 | By Eric Palmer
(http://www.fiercepharmamanufacturing.com)
Commercialization Review Articles